## Slide 1
Prof. John Kimani
EECE 2160: Embedded Design: Enabling Robotics
Many of these slides are adapted by slides developed by David Kaeli (NEU) and Gregory Byrd, NCSU
Bits, Data Types, and Operations

## Slide 2: How do we represent data in a computer?
At the lowest level, a computer is an electronic machine
  works by controlling the flow of electrons
Easy to recognize two conditions:
  presence of a voltage – we’ll call this state “1”
  absence of a voltage – we’ll call this state “0”
Could base state on value of voltage, but control and detection circuits more complex
  compare turning on a light switch to measuring or regulating voltage

## Slide 3: Computer is a binary digital system
Basic unit of information is the binary digit, or bit
Values with more than two states require multiple bits
  A collection of two bits has four possible states: 00, 01, 10, 11
  A collection of three bits has eight possible states: 000, 001, 010, 011, 100, 101, 110, 111
  A collection of n bits has 2n possible states
Binary (base two) system:
  has two states: 0 and 1
Digital system:
  finite number of symbols

## Slide 4: What kinds of data do we need to represent?
Numbers
  signed, unsigned, integers, floating point, complex, rational, irrational, …
Text
  characters, strings, …
Images
  pixels, colors, shapes, …
Sound
Logical – true, false
Instructions
…
Data type:
  representation and operations within the computer
We will start with numbers…

## Slide 5: Unsigned Integers
Non-positional notation
  could represent a number (“5”) with a string of ones (“11111”)
  problems?
Weighted positional notation
  like decimal numbers: “329”
  “3” is worth 300, because of its position, while “9” is only worth 9
329
102
101
100
101
22
21
20
3x100 + 2x10 + 9x1 = 329
1x4 + 0x2 + 1x1 = 5
most
significant
least
significant

## Slide 6: Unsigned Integers (cont.)
An n-bit unsigned integer represents 2n values:
from 0 to 2n-1
22 | 21 | 20 | 
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 2
0 | 1 | 1 | 3
1 | 0 | 0 | 4
1 | 0 | 1 | 5
1 | 1 | 0 | 6
1 | 1 | 1 | 7

## Slide 7: Unsigned Binary Arithmetic
Base-2 addition – just like base-10!
  add from right to left, propagating carry
10010 10010 1111
+ 1001 + 1011 + 1
11011 11101 10000
10111
+ 111
carry
Subtraction, multiplication, division,…

## Slide 8: Signed Integers
With n bits, we have 2n distinct values
  assign about half to positive integers (1 through 2n-1) and about half to negative (- 2n-1 through -1)
  that leaves two values: one for 0, and one extra
Positive integers
  just like unsigned – zero in most significant bit 00101 = 5
Negative integers
  sign-magnitude – set top bit to show negative, other bits are the same as unsigned 10101 = -5
  one’s complement – flip every bit to represent negative 11010 = -5
  in either case, MS bit indicates sign: 0=positive, 1=negative

## Slide 9: Two’s Complement
Problems with sign-magnitude and 1’s complement
  two representations of zero (+0 and –0)
  arithmetic circuits are complex
    How to add two sign-magnitude numbers?
      e.g., try 2 + (-3)
    How to add to one’s complement numbers?
      e.g., try 4 + (-3)
Two’s complement representation developed to make circuits easy for arithmetic
  for each positive number (X), assign value to its negative (-X), such that X + (-X) = 0 with “normal” addition, ignoring carry out
00101 (5) 01001 (9)
+ 11011 (-5) + (-9)
00000 (0) 00000 (0)

## Slide 10: Two’s Complement Representation
If number is positive or zero,
  normal binary representation, zeroes in upper bit(s)
If number is negative,
  start with positive number
  flip every bit (i.e., take the one’s complement)
  then add one
00101 (5) 01001 (9)
11010 (1’s comp) (1’s comp)
+ 1 + 1
11011 (-5) (-9)

## Slide 11: Two’s Complement Signed Integers
MS bit is sign bit – it has weight –2n-1
Range of an n-bit number: -2n-1 through 2n-1 – 1
  The most negative number (-2n-1) has no positive counterpart
-23 | 22 | 21 | 20 | 
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 3
0 | 1 | 0 | 0 | 4
0 | 1 | 0 | 1 | 5
0 | 1 | 1 | 0 | 6
0 | 1 | 1 | 1 | 7
-23 | 22 | 21 | 20 | 
1 | 0 | 0 | 0 | -8
1 | 0 | 0 | 1 | -7
1 | 0 | 1 | 0 | -6
1 | 0 | 1 | 1 | -5
1 | 1 | 0 | 0 | -4
1 | 1 | 0 | 1 | -3
1 | 1 | 1 | 0 | -2
1 | 1 | 1 | 1 | -1

## Slide 12: Converting Binary (2’s C) to Decimal
If leading bit is one, take two’s complement to get a positive number
Add powers of 2 that have “1” in the corresponding bit positions
If original number was negative, add a minus sign
n | 2n
0 | 1
1 | 2
2 | 4
3 | 8
4 | 16
5 | 32
6 | 64
7 | 128
8 | 256
9 | 512
10 | 1024
X = 01101000two
= 26+25+23 = 64+32+8
= 104ten
Assuming 8-bit 2’s complement numbers

## Slide 13: More Examples
n | 2n
0 | 1
1 | 2
2 | 4
3 | 8
4 | 16
5 | 32
6 | 64
7 | 128
8 | 256
9 | 512
10 | 1024
Assuming 8-bit 2’s complement numbers
X = 00100111two
= 25+22+21+20 = 32+4+2+1
= 39ten
X = 11100110two
-X = 00011010
= 24+23+21 = 16+8+2
= 26ten
X = -26ten

## Slide 14: Converting Decimal to Binary (2’s C)
First Method: Division
Divide by two – remainder is least significant bit
Keep dividing by two until answer is zero, writing remainders from right to left
Append a zero as the MS bit; if original number negative, take two’s complement
X = 104ten 104/2 = 52 r0 bit 0
52/2 = 26 r0 bit 1
26/2 = 13 r0 bit 2
13/2 = 6 r1 bit 3
6/2 = 3 r0 bit 4
3/2 = 1 r1 bit 5
X = 01101000two 1/2 = 0 r1 bit 6

## Slide 15: Converting Decimal to Binary (2’s C)
Second Method: Subtract Powers of Two
Change to positive decimal number
Subtract largest power of two less than or equal to number
Put a one in the corresponding bit position
Keep subtracting until result is zero
Append a zero as MS bit; if original was negative, take two’s complement
X = 104ten 104 - 64 = 40 bit 6
40 - 32 = 8 bit 5
8 - 8 = 0 bit 3
X = 01101000two
n | 2n
0 | 1
1 | 2
2 | 4
3 | 8
4 | 16
5 | 32
6 | 64
7 | 128
8 | 256
9 | 512
10 | 1024

## Slide 16: Hexadecimal Notation
It is often convenient to write binary (base-2) numbers as hexadecimal (base-16) numbers instead.
  fewer digits -- four bits per hex digit
  less error prone -- easy to corrupt long string of 1’s and 0’s
Binary | Hex | Decimal
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
Binary | Hex | Decimal
1000 | 8 | 8
1001 | 9 | 9
1010 | A | 10
1011 | B | 11
1100 | C | 12
1101 | D | 13
1110 | E | 14
1111 | F | 15

## Slide 17: Converting from Binary to Hexadecimal
Every four bits is a hex digit.
  start grouping from right-hand side
0011 1010 1000 1111 0100 1101 0111
7
D
4
F
8
A
3
This is not a new machine representation, just a convenient way to write the number

## Slide 18: Operations: Arithmetic and Logical
Recall: a data type includes representation and operations
We now have a good representation for signed integers, so let’s look at some arithmetic operations:
  Addition
  Subtraction
  Sign Extension
We’ll also look at overflow conditions for addition
Multiplication, division, etc., can be built from these basic operations
Logical operations are also useful:
  AND
  OR
  NOT

## Slide 19: Addition
As we’ve discussed, 2’s comp. addition is just binary addition
Assumptions (for now):
  assume all integers have the same number of bits
  ignore carry out
  assume that sum fits in n-bit 2’s comp. representation
01101000 (104) 11110110 (-10)
+ 11110000 (-16) + (-9)
01011000 (88) (-19)
Assuming 8-bit 2’s complement numbers

## Slide 20: Subtraction
Negate subtrahend (2nd no.) and add
Assumptions (for now):
  assume all integers have the same number of bits
  ignore carry out
  assume that sum fits in n-bit 2’s comp. representation
01101000 (104) 11110110 (-10)
- 00010000 (16) - (-9)
01101000 (104) 11110110 (-10)
+ 11110000 (-16) + (9)
01011000 (88) (-1)
Assuming 8-bit 2’s complement numbers

## Slide 21: Sign Extension
To add two numbers, we must represent them with the same number of bits
If we just pad with zeroes on the left:
Instead, replicate the Most Significant Bit (MSB) -- sign bit:
4-bit 8-bit
0100 (4) 00000100 (still 4)
1100 (-4) 00001100 (12, not -4)
4-bit 8-bit
0100 (4) 00000100 (still 4)
1100 (-4) 11111100 (still -4)

## Slide 22: Overflow
If operands are too big, then sum cannot be represented as an n-bit 2’s comp number
We have overflow if:
  signs of both operands are the same, and
  sign of sum is different
Another test -- easy for hardware:
  carry into MS bit does not equal carry out
01000 (8) 11000 (-8)
+ 01001 (9) + 10111 (-9)
10001 (-15) 01111 (+15)

## Slide 23: Logical Operations
Operations on logical TRUE or FALSE
  two states -- takes one bit to represent: TRUE=1, FALSE=0
View n-bit number as a collection of n logical values
  operation applied to each bit independently
A | B | A AND B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | A OR B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | NOT A
0 | 1
1 | 0

## Slide 24: Examples of Logical Operations
AND
  useful for clearing bits
    AND with zero = 0
    AND with one = no change
OR
  useful for setting bits
    OR with zero = no change
    OR with one = 1
NOT
  unary operation -- one argument
  flips every bit
11000101
AND 00001111
00000101
11000101
OR 00001111
11001111
NOT 11000101
00111010

## Slide 25: Text: ASCII Characters
American Standard Code for Information Interchange-ASCII
  Maps 128 characters to 7-bit code.
  both printable and non-printable (ESC, DEL, …) characters
00 | nul | 10 | dle | 20 | sp | 30 | 0 | 40 | @ | 50 | P | 60 | ` | 70 | p
01 | soh | 11 | dc1 | 21 | ! | 31 | 1 | 41 | A | 51 | Q | 61 | a | 71 | q
02 | stx | 12 | dc2 | 22 | " | 32 | 2 | 42 | B | 52 | R | 62 | b | 72 | r
03 | etx | 13 | dc3 | 23 | # | 33 | 3 | 43 | C | 53 | S | 63 | c | 73 | s
04 | eot | 14 | dc4 | 24 | $ | 34 | 4 | 44 | D | 54 | T | 64 | d | 74 | t
05 | enq | 15 | nak | 25 | % | 35 | 5 | 45 | E | 55 | U | 65 | e | 75 | u
06 | ack | 16 | syn | 26 | & | 36 | 6 | 46 | F | 56 | V | 66 | f | 76 | v
07 | bel | 17 | etb | 27 | ' | 37 | 7 | 47 | G | 57 | W | 67 | g | 77 | w
08 | bs | 18 | can | 28 | ( | 38 | 8 | 48 | H | 58 | X | 68 | h | 78 | x
09 | ht | 19 | em | 29 | ) | 39 | 9 | 49 | I | 59 | Y | 69 | i | 79 | y
0a | nl | 1a | sub | 2a | * | 3a | : | 4a | J | 5a | Z | 6a | j | 7a | z
0b | vt | 1b | esc | 2b | + | 3b | ; | 4b | K | 5b | [ | 6b | k | 7b | {
0c | np | 1c | fs | 2c | , | 3c | < | 4c | L | 5c | \ | 6c | l | 7c | ¦
0d | cr | 1d | gs | 2d | - | 3d | = | 4d | M | 5d | ] | 6d | m | 7d | }
0e | so | 1e | rs | 2e | . | 3e | > | 4e | N | 5e | ^ | 6e | n | 7e | ~
0f | si | 1f | us | 2f | / | 3f | ? | 4f | O | 5f | _ | 6f | o | 7f | del

## Slide 26
C-Data Types
Sizes of C-Data types depend on architecture and compiler (options), E.g. 32bit processor:
Size definitions
    b: Bit (e.g. 1kb = 1024 * 1 bit = 1024bits)
    B: Byte (e.g. 3MB = 1024*1024 * 3byte = 3,145,728 bytes
    = 25,165,824 bits)
    Nibble = 4 bits.
Type | Size [Bytes] |  | Type | Size [Bytes]
signed char | 1 |  | unsigned short | 2
unsigned char | 1 |  | signed int | 4
signed short | 2 |  | unsigned int | 4

## Slide 27
Summary
Computers operate in binary
  Conversion from / to binary
Negative number representation
  Two’s complement
Arithmetic and logical operations
Hexa-decimal representation (convenient for user)
ASCII character representation
C-Data types