## Slide 1
Prof. John Kimani
EECE 2160: Embedded Design: Enabling Robotics
Embedded Programming:
Memory-Mapped I/O

## Slide 2: CPU and devices communication
CPU views I/O devices as a set of special-purpose registers
  Status registers: Provides the status of the I/O device
  Control registers: Used by CPU to control the device
  Data registers: Used to read/send date to I/O device
Each I/O register must have an address for the CPU to read or write to.

## Slide 3: CPU and devices communication
Device controller: Logic circuit containing the I/O registers
Device drivers: Software that communicates with the device controller
Device controller
Control register
Status register
Data register
Device
CPU

## Slide 4: How do the CPU and devices communicate?
We have two choices
  Memory ports – utilize reserved instructions to read/write to devices
  Memory mapping – dedicating addresses in physical memory to specific devices
A device driver, a software abstraction, can be used to hide this implementation
In the end, hardware registers on the device need to be read/written to perform communication

## Slide 5: How do the CPU and devices communicate?
Bus-based systems have an address space
  Often times called “memory space”
Specific devices are associated with specific address ranges
Addresses mean different things for different types of devices
  Memory - individual storage locations
  IP cores - register based storage/command locations
How does a CPU access a bus?
  HINT - instruction type?

## Slide 6: Memory-Mapped I/O
Same address space is shared by memory and I/O devices
Address space
ROM
RAM
I/O
CPU
Address
Data

## Slide 7: CPU and devices communicate?
Some CPUs have a separate address space for I/O devices (Isolated I/O). This requires separate instructions to perform I/O operations.
Other architectures use memory-mapped I/O. When using memory-mapped I/O, the same address space is shared by memory and I/O devices. Some addresses represent memory cells, while others represent registers in I/O devices. No separate I/O instructions are needed in a CPU that uses memory-mapped I/O. Instead, we can perform I/O operations using any instruction that can reference memory.

## Slide 8: What is Memory-mapped I/O?
Memory-mapped I/O is the process of either…
  Sending output to a memory-mapped location
  Getting input from a memory-mapped location
The CPU is able to do this using…
  LOAD and STORE instructions
  Essentially, performing writes and reads on the bus
  This is an easy and universal way for a CPU to communicate with other devices

## Slide 9: What can I use memory-mapped I/O for?
Memory devices:
  Storing/retrieving data.
Peripheral devices:
  Sending/receiving data.
  Controlling device (modes, setup, etc.).
HW Accelerators:
  Setting up and controlling the execution of specialized HW circuits.
External devices:
  Reading switch and button settings.
  Controlling LEDs.
  The list goes on and on…

## Slide 10: Memory-mapped I/O
The address space is divided into two parts.
  Some addresses refer to physical memory locations.
  Other addresses actually reference I/O device registers.
When the bus sees certain addresses, it knows they are not memory addresses, but are addresses for accessing I/O devices
  For instance, 0x400D014C is attached Switch1 and 0x400D012C to LED1 on the Zedboard.
Memory
I/O
Memory
C000
D000
FFFF
0000

## Slide 11: Programming memory-mapped I/O
To send data to a device, the CPU writes to the appropriate I/O address. The address and data are then transmitted along the bus.
Each device has to monitor the address bus to see if it is the target.
Control
Address
Data
Hard disks
CD-ROM
Network
Display
CPU
Memory

## Slide 12: Isolated I/O
Another approach is to support separate address spaces for memory and I/O devices, with special instructions that access the I/O space.
For instance, 8086 machines have a 32-bit address space.
  Regular instructions like MOV reference RAM.
  The special instructions IN and OUT access a separate 64KB I/O address space.
Main
memory
00000000
FFFFFFFF
I/O
devices
00000000
0000FFFF

## Slide 13: Comparing memory-mapped and isolated I/O
Memory-mapped I/O with a single address space is nice because the same instructions that access memory can also access I/O devices.
  For example, issuing ARM STR instructions to the proper addresses can store data to an external device.
With isolated I/O, special instructions are used to access devices.
  This is less flexible for programming.

## Slide 14: Using memory-mapped I/O
Memory mapping is done using the mmap system call below:
void *mmap(void *start, size_t length,
Int prot, int flags, int fd, off_t offset);
  start – The address at which to create the mapping. If the value passed in is NULL, the kernel will choose the address for you.
  prot – The desired memory protection of the mapping
  flags – Determines whether updates to the mapping are visible to other processes mapping the same region, and whether updates are carried through to the underlying file.
  The contents of the shared segment are initialized using length bytes starting at offset in the file referred to by the file descriptor fd.
On success, this call returns a pointer to the memory mapped area. In the case of an error, it returns -1.

## Slide 15: Advantages of Memory Mapped I/O
cheaper, faster, easier to build, consumes less power and can be physically smaller
regular memory instructions are used to address devices, all of the CPU's addressing modes are available for the I/O as well as the memory
Takes some memory locations
  Very few compared to the size of the main memory

## Slide 16: Memory Mapped I/O Example
#include <iostream> // Needed for cout, cin, etc.
#include <stdlib.h> // Needed for memory allocation and checking
#include <fcntl.h> // manipulate file descriptor
#include <sys/mman.h> // Needed for System memory management
#include <unistd.h> //Needed for symbols and other funtions e.g usleep()
using namespace std;
// physical base address of GPIO
const unsigned gpio_address = 0x400d0000;
// length of MEM Mapped IO window
const unsigned gpio_size = 0xff;
const int gpio_led1_offset = 0x12C; // Offset for LED1
const int gpio_led2_offset = 0x130; // Offset for LED2
…
…
void RegisterWrite(char *pBase, int offset, int value) {
* (int *) (pBase + offset) = value; } // write value to register
int RegisterRead(char *pBase, int offset) {
return * (int *) (pBase + offset); // read value of register
}

## Slide 17: Example continues…
int main()
{
cout <<"\n----------- LED Testing: -------------\n\n";
int fd = open( "/dev/mem", O_RDWR); // open device memory
// map I/O location
unsigned char *test_base = (unsigned char*)mmap(NULL, gpio_size, PROT_READ | PROT_WRITE, MAP_SHARED, fd, gpio_address);
// Check error
if (pBase == MAP_FAILED)
{
cerr << "Mapping I/O memory failed - Did you run with 'sudo'?\n";
exit(1); // Returns 1 to the operating system;
}

## Slide 18: Example continues…
int value = 0;
cout << "Enter a value less than 256: " << endl;
cin >> value;
cout << "value = " << value << endl;
// write values (1 or 0) to LEDs
RegisterWrite(pBase, gpio_led1_offset, value % 2);
RegisterWrite(pBase, gpio_led2_offset, (value / 2) % 2);
RegisterWrite(pBase, gpio_led3_offset, (value / 4) % 2);
RegisterWrite(pBase, gpio_led4_offset, (value / 8) % 2);
RegisterWrite(pBase, gpio_led5_offset, (value / 16) % 2);
RegisterWrite(pBase, gpio_led6_offset, (value / 32) % 2);
RegisterWrite(pBase, gpio_led7_offset, (value / 64) % 2);
RegisterWrite(pBase, gpio_led8_offset, (value / 128) % 2);
// unmap the memory and close device memory
munmap(pBase, gpio_size);
close(fd);
} // end main