## Slide 1
Prof. John Kimani
EECE 2160: Embedded Design: Enabling Robotics
Introduction to Bluetooth & Wireless Communication With the Wii Remote

## Slide 2: Bluetooth Overview
Wireless technology for short-range voice and data communication
Low-cost and low-power
Provides a communication platform between a wide range of “smart” devices
Not limited to “line of sight” communication
  Advantageous for creating Wireless Personal Area Networks

## Slide 3: Bluetooth Applications
Automatic synchronization between mobile and stationary devices
Connecting mobile users to the internet using bluetooth-enabled wire-bound connection ports
Dynamic creation of private networks

## Slide 4: Introduction to Bluetooth
Connect multiple devices
  Excellent for ad-hoc networking
  Devices can create Piconets
  Master / Slave devices can switch roles as needed.
  Devices can range from headsets to keyboards and mice to gaming consoles like Nintendo's Wii gaming console.

## Slide 5: Synchronization
Keep data on different devices synchronized without using a cable
Example:
  Walk into office and have your PDA synch with your laptop on your desk without even taking your PDA out of your briefcase

## Slide 6: Ad Hoc Networks
Up to 8 devices can be actively connected in master/slave configuration
Piconets can be combined to form scatternets providing unlimited device connectivity

## Slide 7: Bluetooth Radio
Uses 2.4 GHz ISM band spread spectrum radio (2400 – 2483.5 MHz)
Advantages
  Free
  Open to everyone worldwide
Disadvantages
  Can be noisy (microwaves, cordless phones, garage door openers)

## Slide 8: Frequency Hopping
In order to mitigate interference, Bluetooth implements frequency hopping
1600 hops per second through 79 1MHz channels
Spreads Bluetooth traffic over the entire ISM band
All slaves in piconet follow the master for frequency hop sequence

## Slide 9: Frequency Hopping (cont.)
Hops every packet
Packets can be 1, 3, or 5 slots long (a slot is 625µs)
Packets are pretty short

## Slide 10: Bluetooth on Linux
Linux distributions using the Linux kernel 2.4.6 and later implement the Open Source bluetooth stack BlueZ.
BlueZ provides different modules for the Linux platform to interface with various bluetooth enabled devices and services.

## Slide 11: Checking out the source
In the BlueZ bluetooth stack there are many modules that are provided to assist in the “pairing” of various bluetooth devices.
Where do they store the passkey for these devices? It has to be in one of the modules.

## Slide 12: Master/Slave relationship
Bluetooth devices have a “master/slave” relationship.
When two bluetooth devices establish a connection between each other they communicate via their Media Access Control (MAC) address.

## Slide 13: Master meet slave
After a connection between bluetooth devices have be established, the “master” device need only request the “slave” by its MAC address to initiate a connection if it becomes severed.

## Slide 14: Wii Remote (Wiimote)
Connect wiimote to the board via bluetooth
Utilizing BlueZ protocol stack for communication between board and peripheral device
Use Wiimote driver to translate the packet into the desired format, including the corresponding button key, and acceleration sensor’s coordinate value.

## Slide 15: Read Wiimote Buttons
/*This program reads values from event2 and prints the code and value.
#include <iostream>
#include <fcntl.h>
int main(){
char buf[32]; //each packet of data is 32 bytes
int evt2Code, evt2Value; // to hold the code and value
int file = open("/dev/input/event2", O_RDONLY); //Opens the event2 file if (file != -1) { return -1;} // If file is not opened successfully
while(1) {
read(file, buf, 32); // read 32 bytes from the file //and put it in the buffer evt2Code = buf[10]; //the code is placed in byte 10
evt2Value = buf[12]; //value in byte 12
cout << "Code = " << code << ", value = " << value << '\n';
}
close(file); // close the file
return 0;
}

## Slide 16: Read Wiimote Buttons Output
/*Sample output from sudo hexdump event2
0000000 02fa 0000 b35e 000b 0001 0067 0001 0000
0000010 02fa 0000 b35e 000b 0000 0000 0000 0000
0000020 02fb 0000 3d57 0000 0001 0067 0000 0000
0000030 02fb 0000 3d57 0000 0000 0000 0000 0000
0000040 02fc 0000 d183 0004 0001 006C 0001 0000
0000050 02fc 0000 d195 0004 0000 0000 0000 0000
00000a0 02fd 0000 8f46 0002 0001 006A 0001 0000
00000b0 02fd 0000 8f58 0002 0000 0000 0000 0000
16 bytes
1 Packet
/*Sample buffer indexing
buffer [1][0] [3][2] [5][4] [7][6] [9][8] [11][10] [13][12] [15][14]
00000a0 02fd 0000 8f46 0002 0001 006A 0001 0000
00000b0 02fd 0000 8f58 0002 0000 0000 0000 0000
Button Code
Value

## Slide 17: Read Wiimote Accelerometer
/*This program reads values from event0 and prints the code and value.
#include <iostream>
#include <fcntl.h>
int main(){
char buf[16]; //each packet of data is 16 bytes
int code; // to hold the code and value
int file = open("/dev/input/event0", O_RDONLY); //Opens the event0 file if (file != -1) { return -1;} // If file is not opened successfully
while(1) {
read(file, buf, 16); // read 32 bytes from the file //and put it in the buffer code = buf[10]; //the code is placed in byte 10 & value in
short acceleration = (buf[13] << 8) + buf[12];//byte 12 and 13
if (code!= 0x0) // ignore the zeroes
cout << "Code = " << code <<", acceleration = " << acceleration << '\n';
}
close(file); // close the file
return 0;
}

## Slide 18: Read Wiimote Accelerometer Output
/*Sample output from sudo hexdump event0
0009080 03a7 0000 782a 0000 0000 0000 0000 0000
0009050 03a7 0000 782a 0000 0003 0003 fff7 ffff
0009060 03a7 0000 782a 0000 0003 0004 002d 0000
0009070 03a7 0000 782a 0000 0003 0005 009a 0000
0009080 03a7 0000 782a 0000 0000 0000 0000 0000
0009090 03a7 0000 be70 0000 0003 0003 fff3 ffff
00090a0 03a7 0000 be70 0000 0003 0004 0028 0000
00090b0 03a7 0000 be70 0000 0003 0005 009b 0000
16 bytes
1 Packet
/*Sample buffer indexing
buffer [1][0] [3][2] [5][4] [7][6] [9][8] [11][10] [13][12] [15][14]
00000a0 03a7 0000 be70 0000 0003 0004 0028 0000
00000b0 03a7 0000 be70 0000 0003 0005 009b 0000
Axis Code
Value